(Title) T/R Switch with 1N4007

The advantages of high speed switching (QSK) without the clatter of relays lead me to investigate the feasibility of a PIN diode T/R relay. In my research I came across the claim that 1N4007 diode had an intrinsic layer added between its P and N Junction to increase the voltage rating of the diode compared to the 1N4004's or 1N4006's. It appears that a number of radios use the 1N4007 for switching including the Elecraft K2 and an excellent article was written by Wes Hayward W7ZOI in QEX (ref 1) and his book Experimental Methods in RF Design Ref (2) and an excellent implementation of the method was done by Gary Johnson WB9JPS (ref 3) which is easier to get access to than the Hayward articles. The switch presented here is designed for up to 50 watts and is intended for a QRP rig or a driver for a linear etc. It has been soak tested at 100 watts though and coped splendidly.

Briefly the PIN diode (fig1) operates on the principle of a positive and negative junction formed on each side of an intrinsic layer of silicon to increase the minority carrier lifetime. Simply this means that when the diode is reverse biased the minority carriers cause the diode to continue to conduct briefly and it acts as a resistor for this period which in a good low frequency PIN diode will be hundreds of nano seconds. Supposedly the 1N4007 was manufactured this way and at 50 or 60 Hz the slow turn off has no effect but does at 2 MHz upwards. It seems to me that originally this may have been the case but I suspect that current manufacturers do not use the original dies and simply make a diode that fits 1 KV PIV and 1 Amp forward current. In my junk box I have a packet of 40 year old 1N4007's and have done all my experimenting with them. An excellent investigation into the minority carrier lifetime of the 1N400x series was done by Jack Smith of Clifton Laboratories (Ref 4) and this whole site is a goldmine of information generously shared with the world. While slow turn off PIN characteristic diodes have huge advantages, any diode will switch RF as long as the forward current is greater than the RF current so maybe the minority carrier lifetime is less important in practice.

PIN diode switches take the form of fig 2. where forward bias applied to the diode causes it to become a very low value resistor and reverse bias causes it to become a small capacitor. The DC bias supply is isolated by the RF chokes and the RF path is through the input and output capacitors and the diode itself. The RF losses are caused by the impedance of the coupling capacitors and the shunting effect of the chokes plus the resistance of the diode. In the turned off state the leakage across the switch is created by the capacitance across the junction of the diode, coupling between the chokes, radiation from the input and general coupling around the circuit. Remember we are looking at achieving around 60 dB of isolation and need to be very careful of layout here. A practical measurement of the 1N4007 showed about .03 dB of forward loss from 1.8 to 50 MHz but the reverse was a disappointing with 40 dB at 1.8 MHz falling to 20 dB at 21 MHz and 14 dB at 50 MHz. This was clearly not acceptable but did prove the switching action of the 1N4007. I also experimented with increasing the reverse voltage on the diode and was surprised to find that raising the reverse voltage from 12 volts to 40 volts only gave a 2 dB overall improvement in isolation and in spite of the reverse voltages of around 120 volts used in the designs in ref 1,2 and 3 the gains for the complexity of providing 120 volts in battery operated QRP equipment etc. were small so I decided to continue the research with 12 volts reverse bias. I next investigated running 100 watts of RF through the switch for an extended period and checking for increased harmonics or close in products compared to no switch At all and no discernible degradation or products were observed with a very small warming of the diode occurring.

The receive port of the Hayward circuit is shown in fig 3a. and it can be seen that 2 diodes have been placed in series to halve the feed-through capacitance when reverse biased with a good resulting improvement but still insufficient for good isolation. See table 1.
Gary Johnson WB9JPS took the Hayward circuit and improved it by adding a shunt diode at the output end as shown in fig3b. The resultant improvement made the isolator good for 1.8 to 50 MHz and a trace of the curve is shown in fig4 for forward conduction and fig5 for reverse.
Condition 1.8 21.0 50.0
Series capacitors only -.04 -.06 -.08
Centre RF block coil -.04 -.07 -.09
Centre coil + damping -.08 -.12 -.14
Input end RF block coil -.27 -.14 -.16
Output end RF block coil -.41 -.15 -.18
Diodes forward biased -.46 -.22 -.26
Diodes reverse biased -88.3 -33.11 -26.83
Diodes rev bias with shunt -83.53 -57.2 -42.36

Ref 1. Electronic Antenna Switching by Wes Hayward, QEX May 1995
Ref 2. Experimental Methods in RF Design [Paperback] by Wes Hayward W7ZOI, Rick Campbell KK7B, and Bob Larkin W7PUA
Publication Date: March 31, 2009 | ISBN-10: 087259923X | ISBN-13: 978-0872599239 | Edition: Revised 1st Edition
Ref 3. http://wb9jps.com/Gary_Johnson/TR_Switch.html
Ref 4. http://www.cliftonlaboratories.com/diode_turn-on_time.htm#1N4007